Installing NON-RT-RIC by Kubernetes
The non-RT RIC is a type of controller. It helps control and improve RAN elements and resources. It includes an AI/ML workflow for model training and updates. It also provides policy-based guidance for applications and features in near-RT RIC.
Primary Goals:
- The primary goal of Non-RT RIC is to support intelligent RAN optimization by providing policy-based guidance, ML model management and enrichment information to the near-RT RIC function so that the RAN can optimize, e.g., RRM under certain conditions.
- It can also perform intelligent radio resource management function in non-real-time interval (i.e., greater than 1 second).
- Non-RT RIC can use data analytics and AI/ML training/inference to determine the RAN optimization actions for which it can leverage SMO services such as data collection and provisioning services of the O-RAN nodes.
- Non-RT-RIC will define and coordinate rApps (Non-RT-RIC applications) to perform Non-RT-RIC tasks.
- Non-RT-RIC will host the A1 interface (between NONRTRIC & near-RT RICs )
- Non-RT-RIC will also host the new R1 interface (between rApps and SMO/NONRTRIC services)
Prerequisites:
1. kubernetes v1.19 +
2. Docker and docker-compose (latest)
3. Helm 3
4. Minimum 8CPU, 16GB RAM and 50GB Disk.

To deploy NON-RT-RIC, first we need to prepare a perfect environment in Kubernetes. In the next step, we will show the Kubernetes installation step by step in both single node and multimode cluster.

Kubernetes:
Kubernetes is a powerful open-source container orchestration platform used for automating the deployment, scaling, and management of containerized applications. It was developed by Google and is now maintained by the Cloud Native Computing Foundation (CNCF). Kubernetes provides a way to manage containerized applications across multiple hosts, ensuring that applications are running and available to users at all times.
Kubernetes has several flavors like kubeadm, minikube, kinds and so on.

Simple Single-node Kubernetes Cluster via kubeadm on Ubuntu 20.04 & 22.04

1.	Install general dependencies
        sudo apt-get update
        sudo apt-get install -y apt-transport-https ca-certificates curl

2.	Install containerd:
Although we have a few container runtimes to choose from, we’re going with containerd. Before we install containerd, we’ll create its configuration file.

 curl -fsSLo containerd-config.toml \
        https://gist.githubusercontent.com/oradwell/31ef858de3ca43addef68ff971f459c2/raw/5099df007eb717a11825c3890a0517892fa12dbf/containerd-config.toml
sudo mkdir /etc/containerd
sudo mv containerd-config.toml /etc/containerd/config.toml

Without delay, you can install containerd from their official GitHub repository as recommended using the following commands:
curl -fsSLo containerd-1.6.14-linux-amd64.tar.gz \
  https://github.com/containerd/containerd/releases/download/v1.6.14/containerd-1.6.14-linux-amd64.tar.gz
# Extract the binaries
sudo tar Cxzvf /usr/local containerd-1.6.14-linux-amd64.tar.gz
# Install containerd as a service
sudo curl -fsSLo /etc/systemd/system/containerd.service \
  https://raw.githubusercontent.com/containerd/containerd/main/containerd.service
sudo systemctl daemon-reload
sudo systemctl enable --now containerd

3.	Install runc:
Installing runc from their official GitHub repository is the recommended way.

curl -fsSLo runc.amd64 \
  https://github.com/opencontainers/runc/releases/download/v1.1.3/runc.amd64
sudo install -m 755 runc.amd64 /usr/local/sbin/runc

4.	Install CNI network plugins
Install Container Network Interface network plugins from their official GitHub repository.

curl -fsSLo cni-plugins-linux-amd64-v1.1.1.tgz \
  https://github.com/containernetworking/plugins/releases/download/v1.1.1/cni-plugins-linux-amd64-v1.1.1.tgz
sudo mkdir -p /opt/cni/bin
sudo tar Cxzvf /opt/cni/bin cni-plugins-linux-amd64-v1.1.1.tgz

5.	Forward IPv4 and let iptables see bridged network traffic
You need to enable overlay and br_netfilter kernel modules. Additionally, you need to allow iptables see bridged network traffic.

cat <<EOF | sudo tee /etc/modules-load.d/k8s.conf
overlay
br_netfilter
EOF

sudo modprobe -a overlay br_netfilter

# sysctl params required by setup, params persist across reboots
cat <<EOF | sudo tee /etc/sysctl.d/k8s.conf
net.bridge.bridge-nf-call-iptables = 1
net.bridge.bridge-nf-call-ip6tables = 1
net.ipv4.ip_forward = 1
EOF

# Apply sysctl params without reboot
sudo sysctl –system

6.	Install kubeadm, kubelet & kubectl
You need to ensure the versions of kubeadm, kubelet and kubectl are compatible.

# Add Kubernetes GPG key
sudo curl -fsSLo /usr/share/keyrings/kubernetes-archive-keyring.gpg \
  https://packages.cloud.google.com/apt/doc/apt-key.gpg

# Add Kubernetes apt repository
echo "deb [signed-by=/usr/share/keyrings/kubernetes-archive-keyring.gpg] https://apt.kubernetes.io/ kubernetes-xenial main" \
  | sudo tee /etc/apt/sources.list.d/kubernetes.list

# Fetch package list
sudo apt-get update
sudo apt-get install -y kubelet kubeadm kubectl

# Prevent them from being updated automatically
sudo apt-mark hold kubelet kubeadm kubectl

7.	Ensure swap is disabled:
You have to disable the swap feature because Kubernetes does not support it. See the GitHub issue regarding swap on Kubernetes for details.

# See if swap is enabled
swapon --show

# Turn off swap
sudo swapoff -a

# Disable swap completely
sudo sed -i -e '/swap/d' /etc/fstab

 For Single node cluster:
Step 1-7 is common for single node and multi node cluster.
8.	Create the cluster using kubeadm
It’s only a single command to initialise the cluster, but it won’t be very functional in single-node environments until we make some changes. Note that we’re providing “–pod-network-cidr” parameter as required by our CNI plugin (Flannel).

sudo kubeadm init --pod-network-cidr=10.244.0.0/16

Possible Error: If there is any error then run
sudo systemctl daemon-reload
sudo systemctl enable --now containerd

9.	Configure kubectl
To access the cluster, we have to configure kubectl.

mkdir -p $HOME/.kube
sudo cp -i /etc/kubernetes/admin.conf $HOME/.kube/config
sudo chown $(id -u):$(id -g) $HOME/.kube/config

10.	Untaint node
We must untaint the node to allow pods to be deployed to our single-node cluster. Otherwise, your pods will be stuck in a pending state.

kubectl taint nodes --all node-role.kubernetes.io/master-
kubectl taint nodes --all node-role.kubernetes.io/control-plane-

note: If not worked
kubectl get nodes
kubectl taint nodes <ip-172-31-89-81> node-role.kubernetes.io/control-plane=:NoSchedule
note: change this “<….>” part according to your node ID.

11.	Install a CNI plugin
For networking to function, you must install a Container Network Interface (CNI) plugin. With this in mind, we’re installing flannel.
Run this:
kubectl apply -f https://raw.githubusercontent.com/coreos/flannel/master/Documentation/kube-flannel.ym

12.	Install helm
Helm is a package manager for Kubernetes. Helm helps you manage Kubernetes applications — Helm Charts help you define, install, and upgrade even the most complex Kubernetes application.
To install our packages, we’re installing helm v3.
curl https://raw.githubusercontent.com/helm/helm/master/scripts/get-helm-3 | bash

13.	Install chartmuseum
curl https://raw.githubusercontent.com/helm/chartmuseum/main/scripts/get-chartmuseum | bash

14.	Install a CSI driver
We need to install a Container Storage Interface (CSI) driver for the storage to work. We’ll install OpenEBS.

# Add openebs repo to helm
helm repo add openebs https://openebs.github.io/charts
kubectl create namespace openebs
helm --namespace=openebs install openebs openebs/openebs
15.	Install a test application
To test the cluster, you can deploy WordPress. Note that we need to specify the storage class provided by our CSI.

# Add bitnami repo to helm
helm repo add bitnami https://charts.bitnami.com/bitnami
helm install wordpress bitnami/wordpress \
  --set=global.storageClass=openebs-hostpath

16.	Connect master node to worker node
Run this in master: out put of this command for joinning worker
kubeadm token create --print-join-command
output:
example: kubeadm join 172.31.89.81:6443 --token gnzyet.cuftjb0shinn193j --discovery-token-ca-cert-hash sha256:fdc65a3170e2caa573becf3dba31dcddaffc183e589def36a0d2a3b6e02ae3

Run that out put in worker node:
kubeadm join 172.31.89.81:6443 --token gnzyet.cuftjb0shinn193j --discovery-token-ca-cert-hash sha256:fdc65a3170e2caa573becf3dba31dcddaffc183e589def36a0d2a3b6e02ae3

17.	Open new terminal and run localhost:

Open new terminal and run this for avoid localhost error:8080
kubectl proxy --port=8080

Refference: https://kubernetes.io/docs/tasks/tools/

Now time to deploy NON RT-RIC
Preparations
Download the the it/dep repository. At time of writing there is no branch for f-release so cloning can be made from master. Pls check if the branch exist before cloning from master.
Clone repo:
git clone "https://gerrit.o-ran-sc.org/r/it/dep"

Configuration of components to install
It is possible to configure which of nonrtric components to install, including the controller and a1 simulators. This configuration is made in the override for the helm package. Edit the following file
Edit override file
<editor> dep/RECIPE_EXAMPLE/NONRTRIC/example_recipe.yaml

The file shown below is a snippet from the override example_recipe.yaml.
All parameters beginning with 'install' can be configured 'true' for enabling installation and 'false' for disabling installation.

For the parameters installNonrtricgateway and installKong, only one can be enabled.

There are many other parameters in the file that may require adaptation to fit a certain environment. For example hostname, namespace and port to message router etc. These integration details are not covered in this guide.

Editor override file
nonrtric:
  installPms: true
  installA1controller: true
  installA1simulator: true
  installControlpanel: true
  installInformationservice: true
  installRappcatalogueservice: true
  installNonrtricgateway: true
  installKong: false
  installDmaapadapterservice: true
  installDmaapmediatorservice: true
  installHelmmanager: true
  installOruclosedlooprecovery: true
  installOdusliceassurance: true
  volume1:
    # Set the size to 0 if you do not need the volume (if you are using Dynamic Volume Provisioning)
    size: 2Gi
    storageClassName: pms-storage
  volume2:
     # Set the size to 0 if you do not need the volume (if you are using Dynamic Volume Provisioning)
    size: 2Gi
    storageClassName: ics-storage
  volume3:
    size: 1Gi
    storageClassName: helmmanager-storage

...
...
...#

Installation
There is a script that packs and installs the components by using the helm command. The installation uses a values override file like the one shown above. This example can be run like this:

Deploy Nonrtric
sudo dep/bin/deploy-nonrtric -f dep/nonrtric/RECIPE_EXAMPLE/example_recipe.yaml

Result of the installation
The installation will create one helm release and all created kubernetes objects will be put in a namespace. This name is 'nonrtric' and cannot be changed.
Once the installation is done you can check the created kubernetes objects by using command kubectl.
Example : Deployed pods when all components are enabled:

Get Pods
>sudo kubectl get po -n nonrtric
NAME READY STATUS RESTARTS AGE
a1-sim-osc-0 1/1 Running 0 12m
a1-sim-osc-1 1/1 Running 0 10m
a1-sim-std-0 1/1 Running 0 12m
a1-sim-std-1 1/1 Running 0 10m
a1-sim-std2-0 1/1 Running 0 12m
a1-sim-std2-1 1/1 Running 0 3m57s
a1controller-64c5b7fc56-hjx6l 1/1 Running 0 12m
controlpanel-6bf7c4bf79-m6hgl 1/1 Running 0 12m
db-76d79cd769-mngm4 1/1 Running 0 12m
dmaapadapterservice-0 1/1 Running 0 12m
dmaapmediatorservice-0 1/1 Running 0 12m
helmmanager-0 1/1 Running 0 12m
informationservice-0 1/1 Running 0 12m
nonrtricgateway-677988d5c7-rfm88 1/1 Running 0 12m
odusliceassurance-cd5b6f568-q89r5 1/1 Running 0 12m
oruclosedlooprecovery-568f867b45-b6zld 1/1 Running 0 12m
policymanagementservice-0 1/1 Running 0 12m
rappcatalogueservice-687d69756c-lvwrg 1/1 Running 0 12m

After successful installation, control panel shows "No Type" as policy type as shown below.